VHDL Coding
Bitmap ROM Generation
G. Neidermeier
04-September-2023

---
Loading External Data
- Converting binary to ASCII hex and using VHDL file IO functions to load and process data (previous tutorial)
- Convert binary data directly to VHDL ROM using an external program (e.g. hex2rom)

---
Bitmap Prep and Conversion
16-bit data, X1 R5 G5 B5
hex2rom -b rgb_16x2.bmp img_rom 7l16s

---
Bitmap Prep and Conversion
- 16-bit data, X1 R5 G5 B5
- Confirm bitmap header size and encoding
hex2rom -b rgb_16x2.bmp img_rom 7l16s

---
Address Generator
- pix_addr <= to_unsigned(
- BMP_HDR_SZ +
- (
- (row_r - imgRow0) * imgW +
- (col_r - imgCol0)
- ),
- pix_addr'length );

---
Sync ROM
Example hex2rom command with option ‘S’ emits ROM that registers the address.
Advantage is the tool may be able to infer a BRAM as opposed to a distributed RAM (async RAMS always infer a D-RAM, which are LUT based and limited too much smaller size than BRAM resources)
hex2rom -b rgb_16x2.bmp img_rom 7l16s
Now the fun starts!

---
Pixel address and data out of sync
The pixel data lags the intended screen location (column) by 1-clock cycle

---
Synthesis Tool Emits DRC Warnings
- The Synthesis tool does its thing based on how it interprets the VHDL code describing the circuit design – the tool makes the final decision as to whether the design is going to result in a properly functioning circuit – for BRAM resources it means the synth tool must see that the inputs will be properly synced to the output
- Consult XST User Guide: BRAMS must be synchronous, i.e. must have registered inputs (or registered outputs, or both depending on the style of RAM that the tool infers)
- Generally the tool can be “coaxed” to infer the desired BRAM by “by the book” VHDL (or Verilog!) coding style.

---
Sim waveform with DRC Errors

---
Simulation Analysis
Registered ROM address, offset on Column so line displays correctly
(technically, is offset 1 pixel to right, so at column 1 not 0)

---
Simulation Analysis
Displayed image row is distorted, the rgb_ena signal is not in sync with image row

---
Analyze Distortion of Displayed BMP
- Requested image origin row=1, col=0
- row and col registered to row_r and row_c to eliminate DRC warnings of BRAM
- pix_addr of bmp pixel 0,0 is $23 (35*2==70) … but …
- Rgb_ena==1 when col_r==0 (pix_addr=23) but A_r internal to ROM is REGISTERED input address thus rbg_out of ROM is delayed 1 clock relative to rgb_ena
- Therefore rgb_ena must be delayed 1 clock in order to be in sync with the output of the ROM (see next slide)