VHDL Image Generator
BMP Image Loader
- G. Neidermeier 19-Feb-2023

---
Loading RAM from File
HDL_Coding_Techniques/rams/rams_2oc.vhd
- ROM wired into mux as new image gen block
- Use as ROM instance, no-write (Din and WE are grounded)

---
Simplified Example of Pixel Addresser
- Pixel address is simply a free running counter and makes a rolling pattern when used this way but adequate for initial test
- Using pixel_y or pixel_x directly needs no additional computation logic and makes a reasonable test of RAM interface

---
Reading file into std_logic_vector
- Modified template with ram type std_logic_vector (instead of bit_vector)
- use ieee.numeric_std instead of std_logic_unsigned
- In addtion to std.textio use ieee.std_logic_textio is also necessary
- read() from input buffer to std_logic_vector
- https://vhdlguide.readthedocs.io/en/latest/vhdl/testbench.html

---
New Component Interface
Reset was wrong way to fix RAM synchronization
row and col registered for correct BRAM synchronization

---
Pixel Addresser

---
Loading Bitmap Header
Only the width and height are read from header (color space etc. assumed)

---
Load Bitmap Image Data to Array
function InitRamFromFile use width and height info obtained from bmp header

---
Using Utilization Reports
- Tool seems to have some limitation in how large the RAM can be if inferred from LUTs
- Longer time to synthesize with larger image data

---
Block RAM Inference
- Inputs to dout must synchronize in order for the tool to infer BRAM
- Tool warns when any input to the RAM could be asynchronously reset
- Required row and col to be registered as they are basically the address input to the BRAM