VHDL Coding
t80 VGA Interfacing
G. Neidermeier 16-August-2023

---
Z80 Interrupts
- This project will have: time based interrupts (Vsync, 60Hz to time s/w operation) and also interrupt handler to service switch inputs.
- Z80 NMI non-maskable is edge triggered, IRQ @ $66
- Z80 INT, this project use Mode 0 to vector $38
- Edge triggered requires additional circuit to latch/un-latch interrupt action
- Use VGA controller to harness Vsync signal for INT source.
- Verify Vsync by deriving 1Hz signal that can be approximately verified with stop watch (so no sophisticated test equipment required).

---
New Project Setup
- New project, top.vhd, import constraints .xdc
- Import clocks_1.vhd
- Create new testbench top_tb.vhd (no ext. I/O ports for testbenches)

---
Counter
Clock/counter ……….
    signal clk_cntr : STD_LOGIC_VECTOR(3 downto 0);
    ...
    clk_vga <= clk_cntr(1); -- vga clock 25 Mhz
    u_clk_div: entity work.counters_1
    port map(
        C => clk,
        CLR => reset,
        Q => clk_cntr
    );

---
VGA Controller
VGA controller ……….
    signal clk_vga : STD_LOGIC;
    signal video_on : STD_LOGIC;
    signal pixel_x : INTEGER;
    signal pixel_y : INTEGER;
    u_vga_control : entity work.vga_controller
    ....
        GENERIC map (
        h_pulse => 96,
        h_bp => 46,
        h_pixels => 640,
        h_fp => 16,
        h_pol => '0',
        v_pulse => 2,
        v_bp => 33,
        v_pixels => 480,
        v_fp => 10,
        v_pol => '0')
        port map(
        pixel_clk => clk_vga, -- 25 Mhz
        reset_n => reset_l,
        h_sync => Hsync,
        v_sync => Vsync,
        disp_ena => video_on,
        column => pixel_x,
        row => pixel_y,
        n_blank => open,
        n_sync => open
        );

---
Sync Signals
External sync signal definitions
set_property -dict { PACKAGE_PIN P19 IOSTANDARD LVCMOS33 } [get_ports Hsync]
set_property -dict { PACKAGE_PIN R19 IOSTANDARD LVCMOS33 } [get_ports Vsync]
        Vsync : out STD_LOGIC;
        Hsync : out STD_LOGIC;
    ....
    u_vga_control :

---
Vsync Signal
- Toggle a register on falling edge of Vsync
- Drive LED with test pulse
    --------------------------------------------------
    -- toggle signal on vsync (active-low falling edge)
    --------------------------------------------------
    process (vsync_int)
    begin
        if vsync_int'event and vsync_int = '0'
        then
        if toggler = '1'
        then
        toggler <= '0';
        else
        toggler <= '1';
        end if;
        end if;
    end process;
    led(15) <= toggler;

---
Import T80 Sources
- T80 configuration used is synchronous (T80s.vhd) and no extended registers (T80_Reg.vhd)
- Copy sources into project!
    --------------------------------------------------
    -- toggle signal on vsync (active-low falling edge)
    --------------------------------------------------
    process (vsync_int)
    begin
        if vsync_int'event and vsync_int = '0'
        then
        if toggler = '1'
        then
        toggler <= '0';
        else
        toggler <= '1';
        end if;
        end if;
    end process;
    led(15) <= toggler;

---
Minimal T80 Circuit
- T80 entity instantiation
- Unused outputs can be left open in VHDL
- Inputs tied to 1 (Vdd) or 0 (GND)
- T80 shows in RTL schematic but synthesis tool will disregard (optimize away) components that have no effect on circuit (i.e. doesn’t drive any outputs)
    u_cpu : entity work.T80s
        port map(
        RESET_n => reset_l,
        CLK_n => clk_cpu,
        WAIT_n => '1', -- cpu_wait_l,
        INT_n => '1', -- cpu_int_l,
        NMI_n => '1', -- cpu_nmi_l,
        BUSRQ_n => '1', -- cpu_busrq_l,
        M1_n => open, -- cpu_m1_l,
        MREQ_n => open, -- cpu_mreq_l,
        IORQ_n => open, -- cpu_iorq_l,
        RD_n => open, -- cpu_rd_l,
        WR_n => open, --cpu_wr_l,
        A => open, -- cpu_addr,
        DI => (others => '0'), -- cpu_data_in,
        DO => open --cpu_data_out
        );

---
Program ROM
- Create the new prog_rom VHDL file in Vivado (no need to populate IO port definitions)
- prog_rom.vhd is added to the project, but will be overwritten by script converting z80 binary to VHDL array
- Internal T80 signals shown in simulation: TState, M1, RFSH, Address
- ROM connected to T80 address bus (ROM data out is still N.C.)
    --------------------------------------------------
    -- internal program ROM
    --------------------------------------------------
    u_program_rom : entity work.prog_rom
      port map (
        Clk => clk_cpu,
        A => cpu_addr(5 downto 0),
        D => open
        );

---
Data Bus
- Data bus signal prog_rom_data from ROM to CPU
    u_cpu : entity work.T80s
        port map(
        RESET_n => reset_l,
        CLK_n => clk_cpu,
        WAIT_n => '1',
        INT_n => '1',
        NMI_n => '1',
        BUSRQ_n => '1',
        M1_n => open,
        MREQ_n => open,
        IORQ_n => open,
        RD_n => open,
        WR_n => open,
        A => cpu_addr,
        DI => prog_rom_data,
        DO => open --cpu_data_out
        );
    --------------------------------------------------
    -- internal program ROM
    --------------------------------------------------
    u_program_rom : entity work.prog_rom
      port map (
        Clk => clk_cpu,
        A => cpu_addr(5 downto 0),
        D => prog_rom_data
        );