VHDL Coding
T80 Interrupt Handler
G. Neidermeier 20-August-2023

---
Z80 Interrupts
- This project will have: time based interrupts (Vsync, 60Hz to time s/w operation) and also interrupt handler to service switch inputs.
- Z80 NMI non-maskable is edge triggered, IRQ @ $66
- Z80 INT, this project use Mode 0 to vector $38
- Edge triggered requires additional circuit to latch/un-latch interrupt action
- Use VGA controller to harness Vsync signal for INT source.
- Verify Vsync by deriving 1Hz signal that can be approximately verified with stop watch (so no sophisticated test equipment required).

---
New Project Setup
- New project, top.vhd, import constraints .xdc
- Import clocks_1.vhd
- Create new testbench top_tb.vhd (no ext. I/O ports for testbenches)

---
Clock Divider
- Counter provides VGA dot-clock @ 25Mhz
- Counter provides CPU clock @ 6.25Mhz
    signal clk_cntr : STD_LOGIC_VECTOR(3 downto 0);
    ...
    clk_vga <= clk_cntr(1); -- vga clock 25 Mhz
    u_clk_div: entity work.counters_1
    port map(
        C => clk,
        CLR => reset,
        Q => clk_cntr
    );

---
VGA Controller
Use Vsync signal from VGA controller as INT source
    signal clk_vga : STD_LOGIC;
    ....
    u_vga_control : entity work.vga_controller
    ....
        GENERIC map (
        h_pulse => 96,
        h_bp => 46,
        h_pixels => 640,
        h_fp => 16,
        h_pol => '0',
        v_pulse => 2,
        v_bp => 33,
        v_pixels => 480,
        v_fp => 10,
        v_pol => '0')
        port map(
        pixel_clk => clk_vga, -- 25 Mhz
        reset_n => reset_l,
        h_sync => Hsync,
        v_sync => Vsync,
        disp_ena => video_on,
        column => pixel_x,
        row => pixel_y,
        n_blank => open,
        n_sync => open
        );

---
Sync Signals
External sync signal definitions
set_property -dict { PACKAGE_PIN P19 IOSTANDARD LVCMOS33 } [get_ports Hsync]
set_property -dict { PACKAGE_PIN R19 IOSTANDARD LVCMOS33 } [get_ports Vsync]
        Vsync : out STD_LOGIC;
        Hsync : out STD_LOGIC;
    ....
    u_vga_control :

---
Import T80 Sources
- T80 configuration used is synchronous (T80s.vhd) and no extended registers (T80_Reg.vhd)
- Copy sources into project!
    --------------------------------------------------
    -- toggle signal on vsync (active-low falling edge)
    --------------------------------------------------
    process (vsync_int)
    begin
        if vsync_int'event and vsync_int = '0'
        then
        if toggler = '1'
        then
        toggler <= '0';
        else
        toggler <= '1';
        end if;
        end if;
    end process;
    led(15) <= toggler;

---
Z80 INT Timing
- Z80 INT response from Z80 CPU User Manual UM008011-0816

---
Z80 INT Simulation
- INT register circuit, Hsync as INT source, cpu_int_l signal to T80
- INT register circuit clears cpu_int_l when M1==0 and IOREQ==0
- See address trace PC pushes to stack ($83FF, $83FE)
- INT vector $0038 placed on PC

---
INT Register Circuit
    --------------------------------------------------
    u_cpu : entity work.T80s
        port map(
        RESET_n => reset_l,
        CLK_n => clk_cpu,
        WAIT_n => '1',
        INT_n => cpu_int_l,
        NMI_n => '1',
        BUSRQ_n => '1',
        M1_n => cpu_m1_l,
        MREQ_n => cpu_mreq_l,
        IORQ_n => cpu_ioreq_l,
        RD_n => open, -- cpu_rd_l,
        WR_n => cpu_wr_l,
        A => cpu_addr,
        DI => cpu_data_in,
        DO => cpu_data_out
        );
    -- Register /INT
    u_int_reg : entity work.registers_2
        port map(
        C => vsync_int,
        D => '1',
        CLR => int_reg_clr,
        Q => int_reg_out
        );
        cpu_int_l <= NOT(int_reg_out); –– inverted to CPU
        int_reg_clr <= not (cpu_ioreq_l or cpu_m1_l);
Z80 INT response is level detected, circuit has to de-assert INT after allowing Z80 to set its internal INT flip-flop

---
Z80 Assembly for ISR
org 0
  di
  ld sp, l_stack_top
  jp l_entry ; jump past ISRs
ds 0x0038-$
org 0x0038
  di
  exx ; exchange BC, DE, HL with shadow regs
  ex af, af' ; save AF
  ; do something!
  exx ; restore BC, DE, and HL
  ex af, af' ; restore AF
  ei
  ret ; return from interrupt pops PC
ds 0x0100-$
org 0x0100
l_entry:
   im 1 ; set interrupt mode 1
   Ei ; disable interrupts
  ld hl, l_ram_start
  ; do more stuff ….
- Template for /INT ISR (RST $38)
- ds and org directives for code placement
- /INT vectors to $38 in Z80 interrupt mode 1 (im 1)
- Stack is required, INT response pushes/pops Program Counter