VHDL Image Generator
Vivado Project Setup
- G. Neidermeier 2/2023

---
Create a New Vivado Project

---
Create Top Source Module

---
Import Basys3 Constraints File to Project
Constraints files for Digilent boards on GitHub:
- https://github.com/Digilent/digilent-xdc
- “Copy constraints files into project”!

---
Board File Selection
Todo Arctix7 vs. Spartan 6 vs. Spartan 3

---
Define top Module
- Architecture name can be left default Behavioral (Arch name has implications but they are not binding or concerning for the moment)
- I/O Port Definitions are optional at this time

---
Set External Pins in Constraints File
Un-comment LED and SW definitions

---
Add VHDL Source to new Module
Logically the LED pins are connected directly to the switches so are updated to the switch states continuously

---
Write Bitstream
- Open RTL Analysis | Schematic
- Select Generate Bitstream to implement synthesized design
- Open Hardware Manager, Open Target, Program Device

---
Process and Reset
The synthesis tool warns when signals should be added to the process sensitivity list