VHDL Coding
Z80 Simulation
G. Neidermeier 06-August-2023

---
New Project Setup
- New project, top.vhd, import constraints .xdc
- Import clocks_1.vhd
- Create new testbench top_tb.vhd (no ext. I/O ports for testbenches)

---
Import T80 VHD Files
- T80 CPU core “Official” (v247) from OpenCores.org (free reg. Req’d)
- Newer versions updated by 3rd parties are to be found in various online FPGA projects and repositories
- Download “Latest version” and unpack .tgz in temp directory
- Import files from trunk/rtl/vhdl/:
  - T80s.vhd (synchronous version)
  - T80.vhd
  - T80_MCode.vhd
  - T80_ALU.vhd
  - T80_Reg.vhd (not extended register set)
  - T80_Pack.vhd (T80 package library)

---
Instantiate T80 Minimal Connections
- T80 can be seen in the RTL schematic at this point
- Synthesis run can complete but Run Implementation (Place Design) ends in error all leaf cells are optimized away

---
Code to VHDL ROM
- Loading external data to RAM array within VHDL (textio) – slow to synthesize
- Generating RAM/ROM .vhdl entity directly from bin, hex or srec: synthesize time is shorter
- See t80/trunk/sw/hex2rom.cpp
- In Ubuntu, z80asm and z80dasm can be installed into the environment with apt package manager
org 0
  ld hl, ram_start ;0100 21 00 80
  ld a, 55 ;0103 3e 37 a:=37h
l_loop:
  ld (hl),a ;0105 77
  inc a ;0106 3c
  inc hl ;0107 23
  jr l_loop ;0108 18 fb (jr $-3)
org 0x8000
ram_start:
  db 00

---
Code to VHDL ROM
org 0
  ld hl, ram_start ;0100 21 00 80
  ld a, 55 ;0103 3e 37 a:=37h
l_loop:
  ld (hl),a ;0105 77
  inc a ;0106 3c
  inc hl ;0107 23
  jr l_loop ;0108 18 fb (jr $-3)
org 0x8000
ram_start:
  db 00
6l8s:
6-bit address
LSB-first
8-bit data
Synchronous RAM (registered address)
Generate new VHDL entity prog_rom:
hex2rom -b a.bin prog_rom 6l8s > t80_vga/t80_vga.srcs/sources_1/new/prog_rom.vhd
Example VHDL entity has been written to prog_rom.vhd
Import prog_rom.vhd into Vivado project

---
RAM and Address Map
- Import rams_08.vhd
- Use simplest set of signals to read code from ROM and write test pattern (counter) to RAM
- No address decoding (memory mapping) is used
- RAM is written when WE (logic high)
- MREQ_n == 0 AND WR_n == 0
- Boolean logically equivalent to !(mreq_l or wr_l) because WE is logic high input signal to RAM

---
RAM and Address Map
RAM is written when WE (logic high)
MREQ_n == 0 AND WR_n == 0
Demonstrates rams_08 used "as-is" 16-bit data
ram_data_in(7 downto 0) <= cpu_data_out;

---
T80 Timing Analysis
org 0
  ld hl,ram_start ;0000 21 00 80
  xor a ;0003 af a := 0
loop:
  ld (hl),a ;0004 77
  inc a ;0005 3c
  inc hl ;0006 23
  jr loop ;0007 18 fb (jr $-3)
org 0x8000
ram_start:
   db 00
- 5 op-codes in loop code, but R cycles add to total operations (clock cycles) in loop
- 4.16 us loop execution time
- OSC = 1/100Mhz = 100Ns
- CPUclk = 160nS = 1/6.25Mhz
- About 26 clock cycles: 4.16us / 160ns
- .00000416ns x 65536 = 0.273 s (A15 blinks ~ 3.7 Hz)

---
CPU Clock Detail
- ½ CPU clock = 80 ns but propogation/gate delay 5ns ?
- Counter increments on rising edge of Clock

---
M-cycle, Op-code Fetch (i)
org 0
  ld hl,ram_start ;0100 21 00 80
; xor a ; af a := 0
  ld a, 55 ;0103 3e 37 a:=37h
loop:
  ld (hl),a ;0105 77
  inc a ;0106 3c
  inc hl ;0107 23
  jr loop ;0108 18 fb (jr $-3)
org 0x8000
ram_start:
  db 00

---
M-cycle, Op-code Fetch (ii)
org 0
  ld hl, ram_start ;0100 21 00 80
  ld a, 55 ;0103 3e 37 a:=37h
l_loop:
  ld (hl),a ;0105 77
  inc a ;0106 3c
  inc hl ;0107 23
  jr l_loop ;0108 18 fb (jr $-3)
org 0x8000
ram_start:
  db 00