VHDL Image Generator
Sync Pulse and Test Pattern
- G. Neidermeier 11-Feb-2023

---
VGA Sync Module
- Create new VHDL source vga_controller
- https://forum.digikey.com/uploads/short-url/oX3vXrpTEHSpARgOK6ZrA00sBd.vhd
- VGA sync @ ~25 Mhz
- Basys3 has 100 Mhz system clock
- Timing parameters modified for VGA 640x480 60Hz

---
- Define Hsync, Vsync, and VGA (12-bits) output ports
- Define signals for video enable and pixel x, y

---
Instantiate vga_controller

---
- Enable Sync and VGA signal constraints

---
Drive display with simple image generator circuit (switch inputs)

---
RTL Schematic
Runtime Logic portrays logically equivalent circuit layout for design analysis