VHDL Image Generator
Clock Generator and External Signal Testing
G. Neidermeier 11-FEB-2023

---
Clock Generator Component
- https://surf-vhdl.com/how-to-implement-clock-divider-vhdl/#Figure3
- Create a new VHDL file clock_div_pow2
- Module Definition not required

---
Code Formatter
- https://g2384.github.io/work/VHDLformatter.html
- Check \t 4 space
- Module Definition not required
  Keyword Case lower

---
Component Instantiation
    --------------------------------------------------
    -- clocks
    --------------------------------------------------
    u_clocks : entity work.clock_div_pow2
        port map(
        i_clk => clk,
        i_rst => reset_l,
        o_clk_div2 => open,
        o_clk_div4 => clk_vga,
        o_clk_div8 => open,
        o_clk_div16 => clk_vga
        );
Use work library to create instance of clock_div_pow2 Component (more compact syntax)

---
Simulation of Clock Divider
- Simulation Result
- Re-arranged traces show signals under subcomponents

---
Measure Clock Signals
Define output pins in constraints file

---
Measure Clock Signals
- O_JB0 and O_JC0 Out ports added in entity
- Drive O_JB0 and O_JC0 from VGA clock (25 Mhz) and CPU clock (6.25 Mhz)

---
Measure Clock Signals
Scope bandwidth is just barely adequate to verify signal frequencies:
- O_JB0 <= VGA clock (25 Mhz)
- O_JB0 <= CPU clock (6.25 Mhz)