VHDL Image Generator
Video Signal Mux
- G. Neidermeier 12-Feb-2023

---
Import Multiplexer Template
- Import mux example from xstug_examples.zip
- File: HDL_Coding_Techniques/multiplexers/multiplexers_2.vhd
- Imports to sources_1/imports/multiplexers
- Be sure to check Copy sources into project

---
Modify Mux for Video Data Bus
- 4-1 mux example:http://esd.cs.ucr.edu/labs/tutorial/mux.vhd
- Modified to 12-bit vectors
Instantiated with active inputs to I0 and I1 (I2 and I3 are grounded)

---
Create Additional Image Source
- https://forum.digikey.com/t/vga-controller-vhdl/12794
- Import Downloads/vhdl/hw_image_generator.vhd
- Imports to sources_1/imports/vhdl/

---
Video Data Select Source
- Video source 0 is rgb_reg0 from bmp_img_gen
- Video source 1 is rgb_reg_1 from switches
- I0 and I1 inputs to mux from video data bus signals 0 and 1
- Video source select from sw14+sw15

---
Add Source File for ROM
- Xilinx xstug example roms_signal.vhd
- Imports to soc_t80_vga/soc_t80_vga.srcs/sources_1/imports/rams/

---
VGA Pixel Data from ROM
- to_unsigned() converts integer row to unsigned which is the type of pix_address (indexes into ROM)
- clk_in is required port input to clock the ROM
- roms.signal is 20-bitsx128 but only 12-bits are connected to VGA signal output
- Reference for conversions: https://nandland.com/common-vhdl-conversions/#Numeric-Integer-To-Std_Logic_Vector

---
More ROM Addressing
- Define pix_addr as integer
- ROM address from simple counter

---
New and Improved Image Generator
- Add Generic row/column image placement parameters
- Add row/column parameters in place of address
- Generic inputs are initialized to 0 to illustrate that the map assignments take precedence
- Data vector length changed to 12 bits (RGB bus width)
- RGB 8x16 test pattern in ROM size

---
Pixel Address Calculation
- When row is less than imgRow0 then pix_setaddr is reset
- Pixel address increments and data is clocked from ROM when row and column are within image display boundary
- Pixel data is reset to 0 when row and column are outside of image display boundary
But the DRC warning needs to be investigated!

---
Reset RAMB - Design Rule Check Warning
- VGA sync component output signals row, column etc. to ROM which must be sync’d to the same reset
- The reset conditional block clears the data register and the DRC message goes away