VHDL Coding
Bitmap File Loader
G. Neidermeier 06-August-2023

---
Bitmap File Format
- Device independent, uncompressed RGB raster data
- See https://vhdlwhiz.com/read-bmp-file/ and others
- Simple example, 24-bit color (3-byte (24-bit) RGB per pixel)
- Only needs to parse the image W and H from the header and then read in the pixel data to populate an array of std_logic_vector

---
Loading Text Files in VHDL
- Refer to soc_t80_bmp_file.odp and rams_20c.vhd
- Convert .bmp (binary) to text-hex (note: HREAD appears in VHDL-2008 prior to which there is not a hex option with READ)
- Data is read into an array which is then inferred as a memory (LUT based or BRAM depending upon the memory configuration and other details)
od -v -t x1 $RGB_IN | cut -c 9- | tr '\ ' '\n' > $RGB_OUT
use ieee.std_logic_textio.all;
use std.textio.all;

---
Parsing BMP Header
- subtype byte_type
- type header_type is array
- type bmp_info_type (record)
- impure function (as opposed to pure, i.e. no side-effects)
- readline, then hread into header(i)
- Parse bitmap dims from header array (unsigned 32-bit) into bmp_dims.width and bmp_dims.height

---
BMP Image Supporting Data Structures
- bmp_hdr returned from ReadHeader function
- bmp_img_sz from bmp_hdr (to size the array exactly to the image tile size)
- Array of byte_type (8-bit std_logic_vector) is sized bmp_img_sz * 3 (24-bit RGB)
- 24-bit to be converted to 12-bit RGB (rgb444_type) specific to Basys 3 VGA.
- bmp_type to be returned from InitRamFromFile(), providing caller with BMP image dimensions and pixel_data

---
Reading BMP Image Data
- Needs to (re)open the BMP file and “seek” past the header again (no VHDL fn to do this?)
- Read image data - disregard color-depth BPP at this point
- Copy “raw” BMP image data into bmp_data (organized as array of 12-bit vectors)
- Note 12-bit RGB triples take thee 4-most-significant-bits of from 24bpp data
- Return value of function to bmp_data

---
Adress Generator and Pixel Output
- Declare a VHDL variable to simplify integer address generation
- VHDL process sensitive to clk signal
- Test if current pixel location is within desired image boundaries
- dout from .pixel_data array

---
bmp_loader entity Instiantiation
bmp_loader as sub-component of bmp_img_gen