VHDL Coding
Seven Segment Display
G. Neidermeier 22-July-2023

---
Principle of SSD
- Multiplexed operation, only 1 digit at any time is being driven
- Common anode and common cathode flavors
- Each SSD digit common anodes (anodes) connect together so 1 anode (cathode) drive signal per digit
- 7 segments are controlled by individual cathode (or anode) driver signals
- Decimal point has own anode and cathode signals

---
Hex to Segment Translation
- Each of the possible 16 hex characters needs to know what cathodes (segments) are active
- Table lookup 16 sets of anode configurations
- Using an array is one approach, another is a case statement, which the tool likely emits the same RTL either way.

---
Anode Drive Selection
- Only 1 digit active at any time because of multiplexing – the 1 of 4 active digit expressed as 2-bit vector (2^2)
- A decoder enables only 1 of it’s 2^[width of select bus] which we express in VHDL as a vector of width [2^[width of select bus]]
- SSD requires decoder with 4 output signals selected by input bus of 2^2 bits
- The signal to the anodes is active low so the the decoder referred to as “one cold” (as opposed to one hot)
- The 2-bit output-select vector to the decoder is sourced from 2 bits of a free-running counter that fast enough to multiplex the 4-digits of the SSD

---
Digit Selection
- Multiplexer, 4 ports, 4-bits wide
- Displays 8-bit count on 2 SSDs
- 8 switches control 2 SSDs

---
Finished Circuit
4 entity instantiations and 1 process