VHDL Image Generator
BRAM Content from External Data File
G. Neidermeier 18-July-2023

---
Inferenced BRAM
New project:
- HDL_Coding_Techniques/rams/rams_20c.vhd
- HDL_Coding_Techniques/counters/counters_1.vhd
- Copy HDL_Coding_Techniques/rams/rams_20c.data (do not import into project)
- Optional – populate I/O Port Definitions

---
Instantiate Counter
New project:
- HDL_Coding_Techniques/rams/rams_20c.vhd
- Added generic bus size and data width in counters_1.vhd

---
BRAM Content from File
VHDL impure function
- The impure function runs during synthesis
- Can be thought of as a “preprocessor”
- Large data file slows the synthesis tools - better to convert directly to .vhd with some external script/tool/program outside of Vivado

---
Instantiate RAM
u_rom
- Connect addr input to counter (converted to std_logic_vector)
- Connect dout to romdata register

---
RTL Schematic
- dout is n/c
- RTL schematic shows an RTL_RAM and RTL_REG to dout (n/c)
- Synthesis schematic reveals that the tool optimizes away the RAM that is not connected

---
Connect RAM Data
u_rom
- Connect addr input to counter (converted to std_logic_vector)
- Connect led ports to romdata

---
Synthesis Tool Infers RAM
The RAMB18E1 can be invoked explicitly but then the VHDL code is vendor/tool dependant.