VHDL Image Generator Vivado Project Setup
- G. Neidermeier 11-Feb-2023
Revised 13-July-2023

---
Create a New RTL Project
Use New project wizard to create a New Vivado Project
Select Create Project under Quick Start menu
Give new project a name and location
Be sure RTL Project is selected

---
Create Top Source File
Add Sources
Be sure Target language is VHDL
Choose a file name (top is my default for the top-level file)

---
Add Constraints File to Project
Download constraints files for Digilent boards from their GitHub repository:
https://github.com/Digilent/digilent-xdc
Be sure “Copy constraints files into project” is checked

---
Board File Selection
Be sure to download the board files and copy them to the Vivado installation as shown in the setup tutorial.
Note the Arctix7 is pretty much the lowest-spec device in the Xilinx FPGA products!

---
Top Module Definition
- The default Entity name is the name given to the VHDL top file setup in the New Project wizard
- The Architecture name is required but can be left as the wizard default Behavioral
- I/O Port Definitions are optional here but for convenience commonly used ports such as the system clock (e.g. clk) can be configured here and others added later

---
Configure Constraints File
The constraints file informs Vivado’s synthesis tool as to the expected performance of the implemented design in terms of external I/O signal definitions and signal timing tolerances.
This enables the synthesis and implementation tools to perform Design Rules Checks (DRC reports).
Un-comment the following external IO pin definitions in the constraints file:
- Clock signal
- Switches
- LEDs

---
VHDL Hello World
The entity should have the following port definition (all could have been defined in the Top Module Definition as shown on a previous slide):
ENTITY top IS
PORT (
clk : IN STD_LOGIC;
sw : IN STD_LOGIC_VECTOR(15 DOWNTO 0);
led : OUT STD_LOGIC_VECTOR(15 DOWNTO 0)
);
END top;
Fill in the Behavioral implementation by connecting the LEDs directly to the switches, allowing the switch states to update continuously.
begin
    led <= sw; -- LEDs connected directly to switches
end Behavioral;

---
RTL Analysis Schematic
RTL provides the logical view of the system and will be the first indication if anything is egregiously going to be at issue in the final implemented design.
clk is not used, the LEDs are connected directly to the switches - the switch states update continuously, there is no clocked process.

---
Write Bitstream
- Select Generate Bitstream to implement synthesized design
- Open Hardware Manager, Open Target, Program Device

---
Process and Reset
A reset signal is introduced (digital output pin btnC in constraints file)
Inside a process statements occur sequentially. The processes within the Behavioral description happen concurrently.
The synthesis tool warns n_reset should be identified by the process sensitivity list
If the part is programmed it will function as expected (almost), despite the sensitivity warning but this should be corrected!
Reset logic is inverted in this initial design attempt. Buttons are active high on the Basys3. There tends to be an affinity for active low logic in digital design. n_reset signal is introduced, assigned from reset through VHDL inversion operator.
The corrected VHDL updates the process sensitivity list as well as inverting the reset input port to reset on the button press active low

---
VHDL Code Formatter
Vivado does not provide support for automated formatting of VHDL code
https://surf-vhdl.com/how-to-implement-clock-divider-vhdl/#Figure3
Check:
- Keyword Case lowercase
- \Newline after THEN, semicolon
- Customize Indentation