VHDL Image Generator
Clock Generator and External Signal Testing
G. Neidermeier 11-FEB-2023
Revised 12-July-2023

---
Clock Generator Component
Add counters_1.vhdl to the project from the xilinx_xstug_examples

---
Component Instantiation
Use entity-instantiation to create instance of counters_1
https://vhdlwhiz.com/entity-instantiation-and-component-instantiation/
architecture Behavioral of top is
    signal data : std_logic_vector(3 downto 0);
    signal RES : std_logic;
begin
    uclocks: entity work.counters_1
    port map(
        C => clk,
        CLR => RES,
        Q => data
    );
end Behavioral;

---
Simulation of Clock Divider
- Simulation Result
- Re-arranged traces show signals under sub-components

---
Measure Clock Signals
Define output pins in constraints file

---
Measure Clock Signals
- O_JB0 and O_JC0 output ports added in entity
- Drive O_JB0 from div8 clock (25 Mhz)
- Drive O_JC0 from div16 clock (6.25 Mhz)

---
Measure Clock Signals
Scope bandwidth is just barely adequate to verify signal frequencies:
- O_JB0 <= div8 clock (25 Mhz)
- O_JC0 <= div16 clock (6.25 Mhz)

---
VHDL Code Formatter
Vivado does not provide support for automated formatting of VHDL code
https://surf-vhdl.com/how-to-implement-clock-divider-vhdl/#Figure3
Check:
  - Keyword Case lowercase
  - \Newline after THEN, semicolon
  - Customize Indentation

---
Clock Generator Component (Deprecated)
- Create new VHDL project and a top level module (see previous tutorial in soc_t80_vga.odp
- Create a new VHDL file clock_div_pow2
- Reference clock-divider VHDL code: https://surf-vhdl.com/how-to-implement-clock-divider-vhdl/#Figure3