VHDL Image Generator
Sync Pulse and Test Pattern
- G. Neidermeier 11-Feb-2023
Revised 13-July-2023

---
VGA Controller in VHDL
- VGA … blah blah blah
- In the previous tutorial a VHDL counter module was integrated and provides series of clock divisions including a 25 Mhz clock reference suitable for 640x480 VGA pixel clock
- https://forum.digikey.com/t/vga-controller-vhdl/12794
- VGA sync @ ~25 Mhz
- Basys3 has 100 Mhz system clock
There are 2 VHDL files to download from the project website.
vga_controller sets up the pixel_clock and sync timing
hw_image_generator sets up a circuit to put a simple image pattern on the VGA display

---
VGA Controller and Image Generator
There are 2 VHDL files to download from the project website.
vga_controller sets up the pixel_clock and sync timing
vga_controller uses generics to specify the desired video timing (defaults to HD)
hw_image_generator sets up a circuit to put a simple image pattern on the VGA display

---
Clocks and External IO
- Define Hsync, Vsync, and RGB output ports
- Hsync, Vsync are std_logic while RGB are std_logic_vector (4-bits per color)
- Define signals for video_on , pixel_x, pixel_y
- VGA clock is 100 Mhz / 4, derived from counters_1.vhd (from xilinx_xstug_examples-master/HDL_Coding_Techniques/counters)
- External reset signal from BtnC input port

---
IO Constraints
- Enable external Hsync, VSync and RGB ports

---
Component Instantiation
- Use entity-instantiation to create instance of vga_controller and hw_image_gen
- https://vhdlwhiz.com/entity-instantiation-and-component-instantiation/
- Image generator output is 24-bit RGB – rgb24 is “adapter” to 12-bit RGB ports on Basys3

---
RTL Schematic
- Runtime Logic portrays logically equivalent circuit layout for design analysis but doesn’t account for real signal physics i.e. propagation delay
- Synthesized logic is reduced to equivalent of FPGA fabric which is lookup tables and registers (and then other things such as BRAMs, DSP slices etc.)